## Slide 1: Theme 8 Dam Management Managing & Operating Dams Safely, and Enhancing their Functions

## Slide 2: Contents
      Introduction
      Safety Management of Dams
      Dam Operation during Flood
      Dam Operation for Water Supply
      Measures for Rehabilitation and Improvement of Dam Function
      Lessons Learned

## Slide 3: 1. Introduction
History of Dam Construction in Japan
Source: Edited data from Year Book od Dams (Japan Dam Foundation)
Many dams were constructed in the 1960s to 1970s, and more than 50 years have already passed.
It is necessary to manage aging dams efficiently and to maintain or improve their functions as necessary.
Passed more than 50 years

## Slide 4: 2. Dam Safety Management
(1) Standards and Systems for Safety of Dams
Name of Dam | Comple-tion | Acci dent | Type of Dam | Purpose | Damages
Iruka-ike | 1633 | 1868 | Earthfill dam | Irrigation | 941 dead
No.1 Regulating Pond, Komoro Hydropower Station | 1927 | 1928 | Buttress type concrete dam | Hydro-power | 5 dead
Horonai Dam | 1939 | 1941 | Gravity type concrete dam | Hydro-power | 60 dead
Heiwa-ike | 1949 | 1951 | Earthfill dam | Irrigation | 75 dead
Yoake Dam | 1952 | 1953 | Gravity type concrete dam | Hydro-power | -
Taisyo-ike | 1949 | 1953 | Earthfill dam | Irrigation | 105 dead
Wachi Dam | 1968 | 1967 | Gravity type concrete dam | Hydro-power | 1 dead
Fujinuma Dam | 1949 | 2011 | Earthfill dam | Irrigation | 8 dead/ missing
Source: Edited data from the documents of No.21 Expert meeting on future policy and concept of flood management

## Slide 5: 2. Dam Safety Management
(1) Standards and Systems for Safety of Dams
Plan
Design
Construction
Completion
River Administrator permit based on River Law.
(Occupation of Water, Land, Permission of New Construction)
Review and Approved by Dam Basic Design Meeting
(Public Works Research Institute, NILIM, etc.)
Review and Approved by Experts of Public Works Research Institute, NILIM, etc.
Review and Approved of Initial Impounding Test by Dam Basic Design Meeting
Final Inspection and Approval by River Administrator
(Multipurpose Dam) MILT establishes the right to use Dam
Source: Prepared based on "Construction of Multipurpose for Dams" published by Japan Dams
Notes: 図はRiver ActこれをRiver Lawに修正

## Slide 6: 2. Dam Safety Management
Review of Technical Standards Based on Experience of Great Disasters
1. Great Hanshin-Awaji Earthquake (1995)
Static Rigid Body Stability Analysis Method
Design seismic coefficient
Probable Maximum Earthquakes
Level 2 earthquakes
2. Damages due to Excessive Flood
Review and Improvement of:
Information dissemination
Public awareness
Forecasting technology

## Slide 7: 2. Dam Safety Management
Safety Management of Ponds & Small Reservoirs for Irrigation
Fujinuma Dam Failure
(2011 Earthquake)
The Law of Management and Conservation of Ponds and Small Reservoirs for Irrigation (2019)
8 dead, 124 house damaged
Dam was constructed with insufficient compaction & embankment with rich sand
Magnitude of earthquake beyond past experiences
July 2018 collapse of 32 ponds
The Law of Management and Conservation of Ponds and Small Reservoirs for Irrigation (2019)
Source: Brief session by Tohoku University one month after Earthquake dated on 13 April 2011
Notes: Causes of the Break and Plan of Restoring for Fujinuma Dam, Water, Land and Environmental Engineering, Oct. 2015

## Slide 8: 2. Dam Safety Management
(1) Standards and Systems for Safety of Dams
Example of Information Disseminated for the Failure of Ponds and Small Reservoirs and Evacuation by Using Hazard Map
Source: Data of Miyagi Prefecture

## Slide 9: 2. Safety Management of Dams
Sannako Dam Reinforcing against eqrthquake
(Irrigation Water Supply Dam)
Examples of Maintenance and Management of Old Ponds and Small Reservoirs
(1) Standards and Systems for Safety of Dams
Source: Agriculture and Rural Area Improvement Plan in Gunma Prefecture, 2020

## Slide 10: 2. Safety Management of Dams
Patrol & daily inspection
Occasional Inspection
Periodic Inspection
Comprehensive Dam Inspection
Earthquakes, floods
Once in 30 years
Detect deteriorations & damages from long-term viewpoint
Once in 3 years
Inspection of implementation status of maintenance
Inspection of dam structure and its reservoir
(2) Inspection for Dam Safety

## Slide 11: 2. Safety Management of Dams
Tone River Integrated Dam Group Operation Office of MLIT
Office Director
Yanba Dam Management Branch Office
Fujiwara Dam Management Branch Office
Aimata Dam Management Branch Office
Sonohara Dam Management Branch Office
Community Relations Division
Information of Disaster Prevention Division
Research and Development Division
Research Division
Regional Water Management Division
Management Division
Administration Division
(2) Inspection for Dam Safety
Deputy Manager (Administration)
Deputy Manager (Technical) (2persons)
General Management of Conservation Measures
Officer of Conservation Measures (2persons)
Construction Expert
Senior Expert Staff
Special Investigator
Source: Website of Tone River Dams Integrated Management office

## Slide 12: 2. Safety Management of Dams
3 Regular Staffs
Part-time Staffs
3~4 Outsourced Staff
(2) Inspection for Dam Safety
Source: Website of Tone River Dams Integrated Management Office
Branch office of Fujiwara Dam
Notes: Source: Website of Tone River Dams Integrated Management Office

## Slide 13: 3. Dam Operation During Flood
(1) Storage Capacity Allocation and Flood Protection of Multipurpose Dam
Storage Capacity Allocation of Miyagase Dam
Non-flood season: 183 million m3 for water supply
Flood season: flood control space of 45 million m3 , rest for water supply
Source: Pamphlet of Miyagase Dam, Sagami River System Dam Management Office, Kanto Regional Development Bureau, MLIT
Notes: Source: Pamphlet of Miyagase Dam, Sagami River System Dam Management Office, Kanto Regional Development Bureau, MLIT

## Slide 14: 3. Dam Operation During Flood
Annual Reservoir Operation Record of Miyagase Dam
(1) Storage Capacity Allocation and Flood Protection of Multipurpose Dam
Note: Doshi dam will divert its water, when it is expected to start spilling therefrom, to Miayagase dam for storage therein while Miyagase dam will divert its water to Shiroyama dan which is in shortage of stored water to meet the water supply to Tokyo.
Source: Website of Sagami River System Dam Management Office
Notes: Source: Website of Sagami River System Dam Management Office
Note: Doshi dam will divert its water, when it is expected to start spilling therefrom, to Miayagase dam for storage therein while Miyagase dam will divert its water to Shiroyama dan which is in shortage of stored water to meet the water supply to Tokyo.

## Slide 15: 3. Dam Operation During Flood
Flood Protection Plan of Sagami River and Flood Protection by the Miyagase Dam
Example of flood protection – Miyagase Dam
(1) Storage Capacity Allocation and Flood Protection of Multipurpose Dam
Source: Website of Sagami River System Dam Management Office
Peak flood inflow: 1,700 m3/s
Constant release operation: 1600 m3/s
Downstream release amount: 100 m3/s
Notes: Source: Website of Sagami River System Dam Management Office

## Slide 16: 3. Dam Operation During Flood
Flood Protection (Miyagase Dam for Typhoon No.19, 2019)
Example of flood protection – Miyagase Dam
(1) Storage Capacity Allocation and Flood Protection of Multipurpose Dam
Source: States of Dams at Typhon No.19 in 2019, MLIT

## Slide 17: 3. Dam Operation During Flood
(2) Dam Operation during Extraordinary Flood Exceeding the Design Discharge
Source: Hearing from Tone River Dams Integrated Management Office and Notes on Procedure for Operation of Nomura Dam

## Slide 18: 3. Dam Operation During Flood
Hijikawa River Inundation
People in flooded area may not have received dissemination information from Nomura Dam & Kanogawa Dam
July 2018 major flood damage along Hijikawa River (100 year flood)
Proposed Measures to reduce flood damages caused by dam operation
(2) Dam Operation during Extraordinary Flood Exceeding the Design Discharge
Source: MLIT

## Slide 19: 3. Dam Operation During Flood
Advanced Dam Operation during Heavy Flood (Typhoon No.18)
Flood Protection Plan
Qmax=1,360 m3/s
Qout=150 m3/s
Hiyoshi Dam
Typhoon No.18:
Qmax= 1,690 m3/s > Qmax (Plan) =1,360 m3/s
(2) Dam Operation during Extraordinary Flood Exceeding the Design Discharge
Source: Kinki Regional Development Bureau (MLIT)
Hiyoshi dam

## Slide 20: 3. Dam Operation During Flood
Sudden rise in water level during flood
Flood discharge > reservoir capacity, or
Operation of flood discharge gates complicated
Pre-releasing water to lower water level
(3) Operation and Role of Water Supply Dam during Flood
Flood discharge increase significantly
Increase in flood flow velocity
Reservoir needs to store part of flood inflow
Rising water levels upstream
Riverbed upstream has risen due to sedimentation, or
Dam area not large enough
Preliminary discharge
Flood water release cause no adverse effect on flood management downstream
None
Type 1
Type 2
Type 3
Type 4
Classification of Water Supply Dam and Necessary Actions to Release Flood Water
Article 52 of River Law: River administrator has authority to instruct temporary storage of flood water to the owner of the water supply dam

## Slide 21: 3. Dam Operation During Flood
Recent efforts to use reservoir water in water supply dams for flood protection
(3) Operation and Role of Water Supply Dam during Flood
Advance Release Operation of Kusaki Dam at Typhoon No. 18 in 2019 and its Effect
Source: MLIT

## Slide 22: 3. Dam Operation During Flood
(4) Securing Safety for Residents and River Users in Downstream Area
Example of Notification and Information Sharing
(Nomura Dam and Kanogawa Dam)
Source: Summary of Discussions for Verification of Information Sharing on the Operation of Nomura Dam and Kanogawa Dam, November 2018

## Slide 23: 3. Dam Operation During Flood
Warning of discharge release (Twitter)
Real-time dam data of MLIT
(4) Securing Safety for Residents and River Users in Downstream Area
Source: Fujiwara Dam
Source: MLIT

## Slide 24: 4. Dam Operation For Water Supply
(1) Water Supply by Dam
Illustration of Water Supply Enhanced by Dam
Source: MLIT

## Slide 25: 4. Dam Operation For Water Supply
(2) Integrated Operation of Dams
Yagisawa Dam
Aimata Dam
Yanba Dam
Shimokubo Dam
Naramata Dam
Fujiwara Dam
Kusaki Dam
Watarase Flood Control Basin
Dams Operated by the Tone River Dams Integrated Management Office
Yagisawa Dam
Aimata Dam
Yanba Dam
Shimokubo Dam
Watarase Retarding Basin
Naramata Dam
Fujiwara Dam
Kusaki Dam
Sonohara Dam
Integrated Operation of Multiple Dam
Integrated operation by considering the dam’s location, reservoir volumes, and characteristics of the river basin
Example: nine dams managed by national government & Japan Water Agency Tone River basin
Source: Tone River Dams Integrated Management Office

## Slide 26: 5. Measures for Rehabilitation and Improvement of Dam Function
(2) Dam Rehabilitation Technologies in Japan
Cross Section of Dam Body
Source: Sapporo Development and Construction Office, Hokkaido Regional Development Bureau

## Slide 27: 5. Measures for Rehabilitation and Improvement of Dam Function
Reformulation of Reservoir Operation for Tsuruda Dam
Installation of Additional River Outlet Facility by Drilling (Tsuruda Dam)
(2) Dam Rehabilitation Technologies in Japan
Source: Sendai-gawa River Office, MLIT

## Slide 28: 5. Measures for Rehabilitation and Improvement of Dam Function
Rehabilitation Works
Installation of Additional River Outlet Facility by Drilling (Tsuruda Dam)
Drilling of Dam Body
Expanded Discharge Pipe
Existing Energy Dissipator
Existing Power Pipes
(2) Dam Rehabilitation Technologies in Japan
Source: Sendai-gawa River Office, MLIT
Source: Sendai-gawa River Office, MLIT

## Slide 29: 5. Measures for Rehabilitation and Improvement of Dam Function
Restoration Works
Installation of Additional River Outlet Facility by Drilling (Tsuruda Dam)
Expanded Discharge Pipe
(Completed in 2015)
Expanded Energy Dissipator
(Completed in 2015)
Improved Energy Dissipator
(Completed in 2017)
Replacement of Power Pipe
(Completed in 2015)
(2) Dam Rehabilitation Technologies in Japan
Source: Sendai-gawa River Office, MLIT

## Slide 30: 5. Measures for Rehabilitation of Dam & Improvement of its Function
Before and after Restoration
Restoration of Japan’s Oldest Dam (Improvement of Sayama-ike)
History of Restoration Works
(2) Dam Rehabilitation Technologies in Japan
Source: Sayama-ike Dam Talks about History of Civil Engineering, Historical Studies of Civil Engineering No.15
Source: Website of Osaka Prefecture

## Slide 31: 5. Measures for Rehabilitation and Improvement of Dam Function
(3) Technologies for Dam Sediment Control
In Japan, the sediment capacity of reservoirs is determined by estimating the sedimentation volume that will be deposited over 100 years.
Sediment discharge
bypass facility
Sediment Gates
Source: MLIT (left) , Guide for Dam Sediment Control (Draft), Tenryu River Dams Integrated Management Office, Hokuriku Regional Development Bureau, MLIT(right)

## Slide 32: 5. Measures for Rehabilitation and Improvement of Dam Function
"To Restoring Sediment Downstream” (Nagayasuguchi Dam)
2009
2017
(3) Technologies for Dam Sediment Control
Source: Nakagawa River Office

## Slide 33: 6. Lessons Learned (1)
  (1) To secure dam safety, legislation, technical guidelines, and examination system should be established.
  The mechanisms of dam safety should involve thorough examination at each stage, i.e., planning, design, construction, and maintenance. It is important to conduct daily inspections and patrols, as well as periodic inspections, and not to overlook any small changes or signs of risk. The periodic and comprehensive inspections and establishment of extension plans for the service life can improve the management and reduce the lifecycle costs. Because many ponds built in the old days have structural problems, accidents should be prevented through legislation and financial support for the inspection and reinforcement of dam structures.

## Slide 34: 6. Lessons Learned (2)
  (2) To secure a dam and its downstream areas during flooding, operation rules should be followed.
  The operation rules prescribe gate operations and procedures for the patrol and warning methods for downstream areas. They also cover the gate operations for extraordinary floods that exceed the design flood. This is intended to prevent artificial flooding in downstream areas, even under extraordinary floods. The flood inflow should be discharged in the same amount as entering the reservoir. The inflow volume can be obtained from the flood-inflow forecast based on rain radar data. Flood forecasting is effective for introducing and deciding whether to pre-release reservoir water for increasing the flood-protection capacity before floods.
  (3) Integrated operation of multiple dams can ensure an adequate water supply.
  The integrated operation of multiple reservoirs in the basin and reallocation of the reservoir capacity may enhance the reliability of the water supply and improve the river environment.

## Slide 35: 6. Lessons Learned (3)
  (4) Rehabilitation works can extend lifetime and functions of dams.
  Existing dams can be rehabilitated at a relatively low cost, in a short time, and with minimal burdens on nature and society. Additionally, it is possible to improve the dam functions by using the latest software and hardware technologies, e.g., flood forecasting and countermeasures for reservoir sedimentation, dam raising, and the construction of dam-discharging facilities. Some rehabilitation works can be implemented without interfering with the dam operation.